## Slide 1: Overview of TCP/IP
Basic networking protocol concepts
Common TCP/IP protocols
IP addresses and byte orders
6543TGREPCHECK2&&**(11
Readings
  UNP Ch1 and Ch2

## Slide 2: Overview of TCP/IP Protocols
Application layer (email, http, ssh, ftp, etc)
  The things that we use daily.
  Main functionality: run application protocols
Transport layer (TCP, UDP)
  Allows processes (on different machines) to communicate (reliably or unreliably) with each other.
  Main functionality: end-to-end communication (reliability)
Network layer (IPv4, IPv6) 6543TGREPCHECK2&&**(11
  Allows machines to talk to one another
  Main functionality: routing/fragmentation/internetworking
Host to Network layer (Ethernet)
  Allows directly connected machines to talk to one another
  Main functionality: medium access, encoding

## Slide 3: Overview of TCP/IP Protocols
Protocol: rules that govern how peer entities in the same layer (on different machines) communicate.
Each layer provides services to the upper layer defined by the service interface.
  e.g. tcp service interface is defined by a set of system calls: socket, bind, listen, accept, connect, read and write.
The entities that implement each layer can be processes/system calls/hardware/etc.

## Slide 4: Some TCP/IP Protocols
TCP: transmission control protocol
  connection-oriented, reliable, full duplex, byte stream service
UDP: User datagram protocol
  Connectionless, unreliable
IPv4: Internet Protocol, version 4.
  The protocol that glues the Internet together. Provides (unreliable) packet delivery service for TCP, UDP, ICMP, IGMP. 6543tgrepcheck2&&**(11
IPv6: Internet Protocol, version 6.
  128 bits address, newer version of Internet Protocol.
  Will it ever happen?

## Slide 5: Some TCP/IP Protocols
ICMP: Internet Control Message Protocol.
  Handles errors and control information for IP (ping, traceroute).
IGMP: Internet Group Management Protocol.
  Used in IP multicast 6543tgrepcheck2&&**(11
Socket Programming:
  The use of TCP and UDP
    Can also access the lower layers directly (raw socket)

## Slide 6: User Datagram Protocol (UDP)
Unreliable/connectionless service
  Data may be lost, duplicated and reordered.
  Client/server don’t have any long term relation.
Can perform (unreliable) multicast.
Interface 6543tgrepcheck2&&**(11
  socket, bind, sendto, recvfrom
  Can also use the TCP interface (connect/read/write)

## Slide 7: Transmission Control Protocol (TCP)
Connection-oriented, reliable, full duplex, byte stream service
Interface 6543tgrepcheck2&&**(11
  socket, bind, listen, accept, connect, read, write, close.
An analogy
  Socket: telephone
  Bind: assign telephone number to a telephone
  Listen: turn on the ringer so that you can hear the phone call
  Connect: dial a phone number
  Accept: answer the phone
  Read/write: talking
  Close: ???

## Slide 8: Reliable Communications
Realizing reliable communication means a lot:
  Sequence number, acknowledgement, retransmission, timeout (RTT)
  Sliding window protocol for efficiency
  Flow control
  Connection establishment/release

## Slide 9: Basic Functionality of TCP and UDP
Allow processes on different machines to communicate.
  One crucial issue: addressing
    how to identify your peer?
    Two components: identifying the peer machine and identifying the peer process.
  Identifying peer machine: IP address
  A unique identifier for each network interface connected to an IP network.
    A machine may have multiple IP addresses, one for each interface.

## Slide 10: IP Address (IPv4)
32 bit binary number (IPv4)
Represented as "dotted decimal" notation:
  4 decimal values, each representing 8 bits (octet), in the range 0 to 255.
Example:
  Dotted Decimal: 140 .179 .220 .200
  Binary: 10001100.10110011.11011100.11001000

## Slide 11: IP Address Structure
Two parts.
  Network prefix
  Host ID (remaining).
Network Prefix Host ID
0
31

## Slide 12: Identifying Processes
Using PID?
Port - A 16-bit number to identify the application process that is a network endpoint.
Reserved ports or well-known ports (0 to 1023)
  Standard ports for well-known applications.
  Telnet (23), ftp(21), http (80).
  See /etc/services file on any UNIX machine for listing of services on reserved ports
Ephemeral ports (1024-65535)
  For ordinary user-developed programs.

## Slide 13: Identifying Connection
A 5-tuple that completely specifies the two end-points of a connection:
{protocol, local-IP, local-port, remote-IP, remote-port}

## Slide 14: The Byte Order Problem
Two ways to store 16-bit/32-bit integers
Little-endian byte order (e.g. Intel)
Big-endian byte order (E.g. Sparc)
See example1.c
High-order byte Low-order byte
Address A
Address A+1
High-order byte Low-order byte
Address A+1
Address A

## Slide 15: Network-byte Ordering (Cont.)
How do two machines with different byte-orders communicate?
  Using network byte-order
  Network byte-order = big-endian order

## Slide 16: Network-Byte Ordering (Cont’d)
Converting between host and network byte order
  htonl, htons, ntohl, htohs
  See example2.c
    #include <netinet/in.h>
    uint16_t htons(uint16_t host16bitvalue);
    uint32_t htonl(uint32_t host32bitvalue);
    uint16_t ntohs(uint16_t net16bitvalue);
    uint32_t ntohl(uint32_t net32bitvalue);